## Slide 1
RailGuard
Track Geometry Defect Detection, Based upon SIH problem statement SIH25020(2025)
A low-cost automated prototype for real-time detection of gauge widening and cross-level track anomalies
01
Introduction & Problem Statement
02
Real-World Evidence
03
Objectives & System Design
04
Engineering & Build
05
Software & Validation
06
Dashboard, Timeline & Future Scope
1

## Slide 2
01
Introduction & Problem Statement
2

## Slide 3
Problem Statement & Background
1
Derailment Risk
Track geometry defects account for a major share of freight and passenger train derailments globally.
2
Gauge Widening
Rails spread apart beyond permissible tolerances, risking catastrophic wheel drop between structural rails.
3
Cross-Level / Twist
Elevation asymmetry between rails over short distances causes vehicle dynamic instability.
4
Inspection Gaps
Manual track inspection is periodic, labour-intensive, and prone to gaps between maintenance cycles.
3

## Slide 4
The Defect Is Often Small. The Consequence Isn't.
16
Accidents / derailments
linked to deficient track maintenance across selected zones, per national audit findings.
700+
Rail & weld failures
combined rail fractures and weld failures recorded across the same audited sections.
2,93,030cr+
Track-safety allocation
In the financial year(2026-27) the government of Indian government allocated this money for track safety allocation.
4
Source: centre of financial accountability

## Slide 5
What a Rail Defect Can Look Like
SCHEMATIC OVERVIEW · USE THE MODEL TRACK TO RECREATE CONTROLLED DEFECTS
Gauge Widening:
Rails spread apart beyond the standard gap, increasing derailment risk at the widened section.
Cross-Level / Twist:
One rail sits higher than the other, or the track twists over a short distance.
Broken Rail :
A fracture or separation forms in the running rail, often starting from a hidden flaw.
Track Geometry Anomaly:
General alignment or geometry deviation along a stretch of track.
5

## Slide 6
02
Real-World Evidence
6

## Slide 7
When Track Defects Became Real Derailments
DOCUMENTED CASES:
Rail Failure / Old Flaw
A passenger express derailed after several coaches came off the track, resulting in fatalities. The audit record attributed the accident to rail failure from a pre-existing flaw, and noted overdue deep screening and gaps in track-recording coverage.
Rail Fracture
A passenger express derailed after a rail fracture; multiple coaches left the track and passengers were injured. The audit estimated a multi-crore figure in asset damage; the final safety investigation report was still pending.
Joint / Rail Fracture
Several rear coaches of an express service derailed after a fracture near a rail joint, injuring passengers. Follow-up ultrasonic flaw-detection surveys found numerous additional defective welds and rails nearby.
Fatigue Crack → Rail Break
A rail break was traced to a fatigue crack that started at clustered material inclusions and grew to critical length. The investigating authority recommended exploring real-time monitoring of track health.
7

## Slide 8
International Cases & Research Sources
International Cases
A UK rail-accident investigation into a freight-train derailment at a station identified gauge widening as a contributing factor.
An Australian transport-safety investigation into a separate freight derailment identified rail-head fracture and gauge-widening evidence as contributing causes.
Sources Referenced
National Comptroller & Auditor General (CAG) audit report
Commissioner of Railway Safety (CRS) action-taken report
Press Information Bureau (PIB) releases
PRS Legislative Research analysis
UK Rail Accident Investigation Branch (RAIB)
Australian Transport Safety Bureau (ATSB)
8

## Slide 9
Government Spending on Railway Safety
SAFETY-RELATED RAILWAY FIGURES — NOT A DEFECT-SPECIFIC BUDGET
Safety-related expenditure / budget (₹ crore)
Chart: 
| Y1 | Y2 | Y3 | Y4 | Y5 | Y6
Safety expenditure (₹ crore) | 39200 | 87336 | 101662 | 114022 | 117693 | 120389
Track infrastructure safety
Reported allocation in the tens of thousands of crores for the latest budget year.
Track renewals
Tens of thousands of kilometres of track renewed in recent years nationally.
9

## Slide 10
03
Objectives & System Design
10

## Slide 11
Project Objectives & Scope
1
Automated Detection
Build a scaled motorized cart that detects gauge-widening and cross-level/twist anomalies in real time.
2
Low-Cost Design
Use off-the-shelf microcontrollers and accessible sensors to keep the build within a modest student budget.
3
3D-Printed Testbed
Design a modular 3D-printed test track with calibrated defect zones for repeatable validation.
4
Live Web Dashboard
Host an on-board WiFi web server providing real-time telemetry to any laptop or phone.
11

## Slide 12
System Architecture
1
Mechanical Layer
Modular 3D-printed interlocking track with known defect sections. Rolling chassis with flanged wheels driven by a constant-speed DC gear motor.
2
Sensing & Compute
Microcontroller with integrated WiFi. Dual distance sensors (gauge) + 6-DOF IMU (tilt) + rotary encoder (position).
3
Presentation Layer
On-board HTTP web server serving a live HTML dashboard. Real-time fault mapping shows the precise track location of flagged anomalies.
12

## Slide 13
System Working Principle
1
Constant Speed Traversal The motorized cart moves along the track while the position sensor tracks cumulative displacement from the origin.
2
Continuous Gauge Measurement Opposing distance sensors measure the inward distance to each rail flange; the sum deviation indicates gauge widening or narrowing.
3
Cross-Level / Tilt Profiling The IMU measures roll angle in real time to calculate elevation difference across the left and right rails.
4
Real-Time Threshold Evaluation Sampled values are compared against programmed baseline ranges; out-of-bound readings trigger defect flags with distance coordinates.
5
Telemetry Stream Defect records are instantaneously updated to the local web dashboard for remote inspection.
13

## Slide 14
04
Engineering & Build
14

## Slide 15
Methodology Justification
Why Deterministic Threshold Logic?
Track gauge and cross-level tilt are physical, scale-invariant geometric dimensions. Physical safety limits apply directly regardless of scale or AI classification models.
Direct, deterministic numeric comparison eliminates black-box model uncertainty and ensures reliable execution.
Key Advantages for Capstone Scope
Zero Training Data Needed — Eliminates the requirement for thousands of labelled dataset images.
Deterministic Verification — Every flagged defect is traceable to physical mathematical bounds.
Low Computational Overhead — Runs efficiently on microcontrollers without dedicated AI hardware accelerators.
15

## Slide 16
Bill of Materials & Budget
Category | Component | Qty | Function | Est. Cost (Rs.)
Structure | 3D-Printed Track & Cart Chassis (PLA) | 1 set | Modular defect track & rolling body | ~800 – 1,000
Compute | WiFi Microcontroller (ESP32)+Camera+ESP32 | 2 | Sensor reading, decision logic & web server | ~1000
Sensing | Distance Sensors + IMU + Encoder+MPU6050+VL53L0X+GPS(module)+TCRT5000+IR | 8 | Gauge measurement, tilt profiling & position tracking | ~3000
Drive & Power | Geared Motor, Driver & Battery Pack | 1 set | Propulsion, power management & regulation | ~600 – 700
 |  |  | Total Estimated Build Cost | ~Rs.4,500-5000
.
16

## Slide 17
Hardware & Circuit Design
⚡
Power Isolation Architecture
Separate power rails for motor power and sensor/compute logic, sharing a common ground — prevents inductive motor voltage spikes from resetting the microcontroller.
⚡
Signal Conditioning
Resistor voltage dividers adjust sensor logic levels to match the microcontroller's 3.3V GPIO input tolerances, preventing pin degradation.
⚡
Noise Decoupling
Decoupling capacitors suppress electrical noise to ensure stable sensor readings during active motor drive.
17

## Slide 18
05
Software & Validation
PRESENTED BY PRESENTER 5
18

## Slide 19
Firmware & Calibration Approach
Calibration Sketch (Stage 1)
Uploaded first — prints raw sensor readings (distance sum, roll angle) to a serial monitor so real baseline and tolerance values can be measured directly from the printed track.
Baseline noise is recorded on a clean section; peak deviation is recorded by rolling slowly across each known defect section.
Full Detection Firmware (Stage 2)
Reads both distance sensors and the IMU on a fixed sampling interval
Tracks cumulative cart position from encoder pulses
Flags a timestamped, positioned defect when a reading exceeds tolerance
Drives the motor at a constant speed for repeatable traversal
Hosts its own WiFi access point and serves the live dashboard
19

## Slide 20
Software Execution Flow
1. Calibration
Upon power-up on a known standard segment, baseline gauge and roll-angle values are sampled and saved.
→
2. Sampling
High-frequency sampling of left/right distance sensors, 6-axis accelerometer/gyroscope, and wheel encoder pulses during movement.
→
3. Comparison
Evaluation against programmed tolerance bounds for both gauge deviation and roll deviation.
→
4. Dashboard Log
When an anomaly exceeds limits, an event with the exact track position is logged and pushed to the web UI.
20

## Slide 21
Validation & Testing Approach
Test Stage | Simulated Condition | Expected Response | Pass Criterion
Clean Track | Nominal track without defects | Continuous position updating; zero false anomaly flags | 100% true-negative rate
Gauge Defect | Track segment with artificial gauge widening | Flags gauge-widening defect at correct track position | Positional error < 15mm
Cross-Level Defect | Track section with single-rail elevation dip | Flags cross-level/twist anomaly on live dashboard | Correct tilt magnitude detected
Repeatability | 5 consecutive full-track runs | Identical defect locations logged consistently | High repeatability index
21

## Slide 22
06
Dashboard, Timeline & Future Scope
23

## Slide 23
The Live Web Dashboard
What It Shows
Dashboard — track status, defect counter, battery, GPS, latest event
Alerts — full event log with ID, time, type, IR state, GPS, status
Images — camera-capture gallery for each detected abnormality
Sensors — live accelerometer & gyroscope telemetry, IR indicator
Location — GPS map view with a direct Google Maps link
Settings — telemetry, notification & upload toggles
Why It Matters
Hosted directly by the microcontroller's own WiFi access point — no internet needed. The page auto-refreshes so a reviewer watching the dashboard during a live run can see a defect appear, get logged with its exact position, and be pinned on a map in real time.
A “simulate defect” control lets the team demonstrate the alert flow on demand, and a toast-notification system highlights every new event as it happens.
24

## Slide 24
Scalability & Future Scope
↗
Full-Scale Deployment
Mounting inspection pods on revenue train bogies for continuous commercial track scanning.
↗
Optical Crack Scanning
Integrating IR surface scanners paired with high-speed camera triggers to capture rail-head micro-fractures.
↗
GPS & Cellular Telemetry
Replacing the local WiFi dashboard with a GSM/GPS module for cloud-based centralized dispatching.
↗
Energy Harvesting
Harnessing wheel-rotation axle generators for continuous, self-powered autonomous operation.
26

## Slide 25
Thank You
RailGuard: Track Geometry Defect Detection
27